## Slide 1: ELECTRICITY
CHAPTER NUMBER 12
Notes: Welcome to the to the lecture on Electricity

## Slide 2: What is covered in this chapter
Combination of Resistors
Heating effect of electric current and its application
Electric Power
Notes: The topics covered are:
Combination of Resistors
Heating effect of electric current and its application
Electric Power

## Slide 3: Resistance of a system of resistors
Notes: Ways to connect resistors: are
-> Parallel
-> Series
Shown in diagram (a) an electric circuit in which three resistors having resistances R1
,R2,R3and R4, respectively, are joined end to end. Here the resistors are said
to be connected in series.
Total resistance given by :
Resistance=R1+R2+R3+R4
Resistors connected in parallel
As shown in diagram (b) R1,R2,R3,R4 are connected in parallel where we will get combined resistance of all these resistors as
Resistance=1/R1+1/R2+1/R3+1/R4

## Slide 4: Heating effect of electric current
How is heat produced in a circuit?
Heating effect.
Notes: When a battery is connected to an electric circuit the resistance in the circuit which is imposed of the flow of charge produces some heat. The heat produced in using any gadget is the heat effect that the current is producing. Some energy is used in powering up the gadget, the rest is dissipated this is known as the heating effect of electric circuit.

## Slide 5
Power:
P =Q/t=vi
V= voltage
i= current
t=time
Q=charge
Notes: Consider a current I flowing through a resistor of resistance R . Let the potential difference across it be V .Let t be the time during which a charge Q flows across. The work done in moving the charge Q through a potential difference V is VQ . Therefore, the source must supply energy equal to VQ in time t. Hence the power input to the circuit by the source is
P =Q/t=vi
Where :
V= voltage
i= current
t=time
Q=charge

## Slide 6
Formulae
H = Vit
To this equation when we apply ohm’s law we get : H = I^2 Rt
Notes: The energy supplied to the circuit by the source in time t is P × t, that is, VIt. What happens to this energy expended by the source? This energy gets dissipated in the resistor as heat. Thus for a steady current I, the amount of heat H produced in time t is:
H = VIt
To these equation when we apply ohm’s law we get :
H = I^2 Rt
Where H is heat

## Slide 7
Notes: Here we are able to visualize how an electric current when passed through a conductor causes the conductor to becomes hot after some time and produce heat. This happens due to the conversion of some electric energy passing through the conductor into heat energy. This effect of electric current is called heating effect of current.

## Slide 8: ELECTRIC POWER
Power
Electric power
The formulae for power
P = VI Or P = I^2 R = V^ 2 /R
Notes: Power is rate of doing work is power.
Hence similarly
Electric power is rate of consumption of energy is electric power
Formulae that can be driven are
The power P is given by P = VI Or P = I^2 R = V^ 2 /R

## Slide 9
SI unit of power is watt (W)
1 W = 1 volt · 1 ampere = 1 V A
Notes: SI units:
The SI unit of electric power is watt (W). It is the power consumed by a device that carries 1 A of current when operated at a potential difference of 1 V.
1 W = 1 volt · 1 ampere = 1 V A

## Slide 10
1 kW h = 1000 watt *3600 second
The unit ‘watt’ is very small.
Therefore, in actual practice we = 3.6 · 106 watt second
= 3.6 · 106 joule (J)
Notes: The unit ‘watt’ is very small. Therefore, in actual practice we use a much larger unit called ‘kilowatt’.
It is equal to 1000 watts. Since electrical energy is the product of power and time, the unit of electric
energy is, therefore, watt hour (W h).
1 kW h = 1000 watt *3600 second
= 3.6 · 106 watt second
= 3.6 · 106 joule (J)